## Slide 1
Anomaly Detection in Multi-Robot Systems
Exploiting Self-Awareness
(FAIEMA 2023)
1 Doctoral School in Decision Making in a Digital Environment
2 Institute of Networked and Embedded Systems
Mohammad Rahmani 1 and Bernhard Rinner 2

## Slide 2
Introduction
2
Self-awareness (SA) is robots’ ability to model knowledge about “themselves,” in relation to the world
Robots use data from proprioceptive and exteroceptive sensors to build spatiotemporal models
In Multi-robot systems (MRS) such models could be also build about relations such as following
each other whenever there is a narrow corridor
To update or create models they need to detect abnormal experiences
LIDAR
GPS
Exteroceptive sensors
Proprioceptive sensors
model
Most expected observation in
next timestep
Zt
Zt-1
Zt
Current
sensory observation
observation
This distance is a sample
abnormality

## Slide 3
Motivation
3
1
2
Training scenario
Are we
experiencing
a new relation?
(high anomaly?)
New scenario
Anomaly detection to make multiple robots able to detect new spatiotemporal relations
model
for 1
Create
a new model
for 2
yes

## Slide 4
Motivation | A self-aware framework for MRS
4
Preprocessing
Exteroceptive
and
proprioceptive
sensory data
abstracting
state space
Offline
learning
Anomaly
detection
proprioceptive models
exteroceptive models
Create/update models
Online
testing
anomaly

## Slide 5
Related work
5
An SA framework based on MJPF in a single-robot system Regazzoni, B. Rinner et al, “Multisensorial generative and descriptive self-awareness models for autonomous systems,” Proc. of the IEEE 2020
Markov Jump Particle Filter (MJPF) as spatiotemporal model
M. Baydoun et al “Learning switching models for abnormality detection for autonomous driving,”Conference on Information Fusion, 2018.
A hierarchical model applying Particle and Kalman filters based on dynamic Bayesian networks (DBN)
Uses Coupled MJPFs as spatiotemporal models in several scenarios for anomaly detection in MRS
Compares the results with single MJPF
Studies sensors’ noise impact anomaly detection ability
Studies impact of clusters number in state space on anomaly detection
This paper:
Suggesting Coupled MJPFs as a spatiotemporal model in MRS M. Rahmani and B. Rinner, “Towards self-awareness in multi-robot systems,” in Proc. Austrian Robotics Workshop, 2022, pp. 1–2.

## Slide 6
Methodology | Proposed spatiotemporal model
6
Joint
predictions
3-layer hierarchical model based on Coupled Dynamic
Bayesian Networks (CDBN)
Abstract layer (S) in which Particle filter is used for determining
the most probable abstract state
Continuous states (X) that uses a Kalman filter with a constant velocity vector for state estimation inside the abstract state
The interaction layer (D) couples robots for joint predictions

## Slide 7
Methodology | Offline training
Simulate GPS and LIDAR data from a training scenario
Cluster sensory data to quasi-stationary segments
Reduce high dimensional LIDAR
data with neural auto-encoders
1
2
3
4
7
D
Transition Matrix
for D Layer is learned
Cluster
sensor data
counting
Cluster
sensor data

## Slide 8
Methodology | Online inference
New scenario
Robot 1 DBN
Robot 2
DBN
8
High diffrence
btw observation
and prediction
1. Transition matrix D 2. Live sensor data
Joint
prediction
High diffrence
btw observation
and prediction

## Slide 9
Experimental setup
9
Using Robot Operating System (ROS), Gazebo
and CTUMRS framework to simulate two Tarot t650 drones
GPS as proprioceptive sensor
  281k sensory reading
AP2 LIDAR as exteroceptive sensor
  720 dimensional sensory readings reduced to 3 using neural auto encoders.
  120k sensory readings
Anomaly metric: Kullback–Leibler (KL) divergence between CDBN predictions and sensory observations
Tolerance: μ + 3σ of anomaly values in training scenario

## Slide 10
Results | CDBN
10
32 clusters, Gaussian noise 0.0002
LIDAR high anomalies happen before GPS high anomalies
Lidar clusters – reduced 3 dim
GPS clusters

## Slide 11
Aggregated DBN vs Coupled DBN
11
Aggregation suffers from curse of dimensionality and is not scalable
The anomaly values for GPS and LIDAR are 42% and 38% smaller respectively in aggregated approach vs CDBN
This could be interpreted as MRS’s less awareness of new experiences in aggregated approach vs CDBN
Robot 1 observation
Robot 2 observation
Aggregated Robot 1 & 2 observations

## Slide 12
Noise impact on anomaly detection
12
CDBN learning rate reduces when using noisier sensors

## Slide 13
Number of clusters impact on anomaly detection
13
Higher clusters number improves anomaly detection performance

## Slide 14
Conclusion
14
CDBNs performed as reliable spatiotemporal models in our simulations
They perform better than aggregated DBNs in anomaly detection
Higher sensor noise reduces their anomaly detection performance
Higher number of clusters increases their anomaly detection performance
Future work
Proposing an SA framework in MRS which includes
  Pairing relevant exteroceptive and proprioceptive CDBNs
  Creating and updating CDBNs in an MRS
  Choosing the best predicting CDBN according to the most recent sensory observations in MRS